## Slide 1: Trimming Simulation of Forming Metal Sheets Isogeometric Models by Using NURBS Surfaces
D. Herrero-Adan (1), Rui P.R. Cardoso (2), O.B. Adetoro (1)
daniel.herreroadan@uwe.ac.uk
1Department of Engineering Design and Mathematics, University of the West of England, BS16 1QY Bristol, UK
2Department of Mechanical, Aerospace and Civil Engineering, Brunel University London, UB8 3PH Uxbridge, London, UK

## Slide 2: 01.- MOTIVATION 02.- GENERAL VIEW 03.- TRIMMING CURVE DEFINITION 04.- STIFFNESS MATRIX AND FORCES 05.- EXAMPLES 06.- POTENTIAL IMPROVEMENTS

## Slide 3: 01.- MOTIVATION
At the end of forming it is usual to trim the formed part to achieve final shape or to remove edge micro-cracks
Due to plastic deformation during forming residual stresses are generated
After trimming there is a redistribution of the residual stresses and displacements to achieve a new equilibrium
It is necessary to define accurately the trimming line to be able to assess the new state

## Slide 4: 01.- MOTIVATION 02.- GENERAL VIEW 03.- TRIMMING CURVE DEFINITION 04.- STIFFNESS MATRIX AND FORCES 05.- EXAMPLES 06.- POTENTIAL IMPROVEMENTS

## Slide 5: 02.- GENERAL VIEW
0) At the end of forming there are defined:
-Part geometry
-Material properties
-Residual stresses {so}
Stored in surface
model “S”
(Definition of trimming surface “T” - NURBS surface)
1) Surfaces S-T intersection is computed, the output is a trimming curve “C”
2) A portion of S is removed and then deactivated for subsequent calculations as [1]. The remaining surface is called “St”
3) Control points forces due to residual stresses and stiffness matrix are calculated using the remaining area of S (St) in the integrals
4) Final configuration
Target of this job
[1] Kim HJ, Seo YD, Youn SK. Isogeometric analysis for trimmed CAD surfaces. Comput. Methods Appl. Mech. Engrg. 198 (2009) 2982–2995

## Slide 6: 01.- MOTIVATION 02.- GENERAL VIEW 03.- TRIMMING CURVE DEFINITION 04.- STIFFNESS MATRIX AND FORCES 05.- EXAMPLES 06.- POTENTIAL IMPROVEMENTS

## Slide 7: 03.- TRIMMING CURVE DEFINITION
03.1.- Strategy
03.2.- Row of intersection points
03.3.- Curve fitting
03.4.- Definition of remaining surface
03.5.- T surface requirements
Surfaces S and T intersect in physical space but are defined in different parameter spaces
Iterations are required
I .- Calculate a row of S-T intersection points
II .- Fit a curve to the row of intersection points but in S parameter space

## Slide 8: 03.- TRIMMING CURVE DEFINITION
03.1.- Strategy
03.2.- Row of intersection points
03.3.- Curve fitting
03.4.- Definition of remaining surface
03.5.- T surface requirements
Inversion_Point (technique from [2])
Input: P1 : physical coordinates
u1,v1: initial parameter coordinates
Output: P2: closest surface point to P1
(physical and parameter coordinates)
[2] Piegl L, Tiller W. The NURBS Book. Berlin. Springer-Verlag, (1996).
Points_Row [ Bouncing [ Inversion_Point ] ]

## Slide 9: 03.- TRIMMING CURVE DEFINITION
03.1.- Strategy
03.2.- Row of intersection points
03.3.- Curve fitting
03.4.- Definition of remaining surface
03.5.- T surface requirements
Bouncing
Input: initial searching coordinates
P1 : physical coordinates
u1,v1 & c1,d1 : parameter coordinates
Output: P2: closest S-T intersection point to P1
(physical and parameter coordinates)
[2] Piegl L, Tiller W. The NURBS Book. Berlin. Springer-Verlag, (1996).
Points_Row [ Bouncing [ Inversion_Point ] ]
T surface
S surface

## Slide 10: 03.- TRIMMING CURVE DEFINITION
03.1.- Strategy
03.2.- Row of intersection points
03.3.- Curve fitting
03.4.- Definition of remaining surface
03.5.- T surface requirements
Points_Row [ Bouncing [ Inversion_Point ] ]
Points_Row
Input: initial searching coordinates
P0 : physical coordinates
u0,v0 & c0,d0 : parameter coordinates
Output: row of intersection points

## Slide 11: 03.- TRIMMING CURVE DEFINITION
03.1.- Strategy
03.2.- Row of intersection points
03.3.- Curve fitting
03.4.- Definition of remaining surface
03.5.- T surface requirements
Points_Row [ Bouncing [ Inversion_Point ] ]

## Slide 12: 03.- TRIMMING CURVE DEFINITION
03.1.- Strategy
03.2.- Row of intersection points
03.3.- Curve fitting
03.4.- Definition of remaining surface
03.5.- T surface requirements
Parameter
space S
[2] Piegl L, Tiller W. The NURBS Book. Berlin. Springer-Verlag, (1996).
Row of intersection points in parameter space S
Fit a B-spline in parameter space S
“global curve interpolation to point data” [2]
Physical space

## Slide 13: 03.- TRIMMING CURVE DEFINITION
03.1.- Strategy
03.2.- Row of intersection points
03.3.- Curve fitting
03.4.- Definition of remaining surface
03.5.- T surface requirements
Surface on the left hand side of the trimming curve remains
Direction of curve is given by cross product of surfaces S and T normal vectors
Surface on the right hand side is to be removed

## Slide 14: 03.- TRIMMING CURVE DEFINITION
03.1.- Strategy
03.2.- Row of intersection points
03.3.- Curve fitting
03.4.- Definition of remaining surface
03.5.- T surface requirements
Trimming T surface has to:
1.- Be smooth (derivable)
2.- Trim the metal sheet in the physical space
3.- The resulting trimming curve has to enclose a portion of S surface
4.- Extend slightly further than the intersection between the two surfaces
5.- Be open surface

## Slide 15: 01.- MOTIVATION 02.- GENERAL VIEW 03.- TRIMMING CURVE DEFINITION 04.- STIFFNESS MATRIX AND FORCES 05.- EXAMPLES 06.- POTENTIAL IMPROVEMENTS

## Slide 16: 04.- STIFFNESS MATRIX AND FORCES
Already developed for trimmed 2D surfaces by Kim et al. [1]. Here we proceed in a similar manner
[1] Kim HJ, Seo YD, Youn SK. Isogeometric analysis for trimmed CAD surfaces. Comput. Methods Appl. Mech. Engrg. 198 (2009) 2982–2995
When computing [Ke] and {fecp} at each element:
- Ignore totally deactivated elements
- For trimmed elements: divide into triangles remaining area and integrate those triangles
- Integrate in a standard manner totally in elements
Then the control points displacement are calculated and afterwards the stresses

## Slide 17: 01.- MOTIVATION 02.- GENERAL VIEW 03.- TRIMMING CURVE DEFINITION 04.- STIFFNESS MATRIX AND FORCES 05.- EXAMPLES 06.- POTENTIAL IMPROVEMENTS

## Slide 18: 04.- EXAMPLES
Trimming examples:
- slotted pipe:
- end-trimmed pipe:

## Slide 19: 04.- EXAMPLES
Trimming and displacement calculation example:
- Slotted crown quarter :

## Slide 20: 01.- MOTIVATION 02.- GENERAL VIEW 03.- TRIMMING CURVE DEFINITION 04.- STIFFNESS MATRIX AND FORCES 05.- EXAMPLES 06.- POTENTIAL IMPROVEMENTS

## Slide 21: 06.- POTENTIAL IMPROVEMENTS
Algorithm to select the initial searching points
Allow trimming surface to be closed
(simulate holes)
Non-derivable trimming surfaces

## Slide 22: 06.- POTENTIAL IMPROVEMENTS
Remove step dependency for trimming curve
(step length selection)
p=2
p=3
p=4
Step = 25
Step = 5
(Overlapping curves)

## Slide 23: THANK YOU FOR YOUR ATTENTION